## Slide 1
Optimization‑based vulnerability reduction management model for pre-flood reconstruction planning of links in transportation networks considering equity, efficiency, and economic aspects
Farshad Hesamfar

## Slide 2: Introduction
We did not achieve much in terms of preventing nature from triggering on the planet in order to avoid socio-natural hazards such as climate change-induced floods. As a result, alternatives in the context of infrastructure disaster risk reduction are limited to two main concepts: 'reducing vulnerability' and 'increasing resiliency' of infrastructures.
Reducing vulnerability refers to the process of minimizing the susceptibility of infrastructures to damage or disruption caused by natural hazards. It involves identifying and addressing the weaknesses and vulnerabilities of infrastructures, such as their design, construction, and location, to make them more resistant to hazards. The goal is to decrease the likelihood and extent of damage or disruption when a hazard event occurs.
While reducing vulnerability aims to prevent or minimize damage, increasing resiliency focuses on the ability to recover and restore functionality. Both concepts are important in ensuring the long-term sustainability and functionality of infrastructures in the face of natural hazards.

## Slide 3: Introduction
The socioeconomic function of many individuals, enterprise, and critical services depends on the efficient operation of transportation networks (Cova and Cogner 2004).
We define the optimization model for pre-flood reconstruction planning of links in transportation networks considering equity, efficiency, and economic aspects as a prescriptive decision model built to respond to a potential flood that (1) directly causes major operational disruptive impacts on the traffic functionally of the network, and (2) can be alleviated only by physical measures.

## Slide 4: Phases
Problem definition
Prob. structuring
Constraints and decision variables
Prob- formulation
Mathematical model
Variables and factors translation
Multi-objective problem solving
Objectives and attributes
Pareto optimality
Method (solver)
Model Verification and Validation
  Post optimization

## Slide 5: Problem statement
When reconstructing the road network for reducing vulnerability three main dimensions of sustainable management are considered
Minimum cost as economic objective for giving affordable management scenario
Maximum traffic efficiency with minimum travel time to critical facilities, ensuring fast access of demand points
Equity related cost with giving priority to reconstruction of most vulnerable geographical zones (Rawlsian maximin can be incorporated)
Maximum accessibility of demand zones to increase the utility and resiliency of the whole area

## Slide 6: Problem formulation
Formulating a model for equity-based access to critical infrastructures after a flood disaster in different management zones involves optimizing the restoration and allocation of resources to ensure equitable access while considering the efficiency, repair costs, accessibility, and specific constraints and objectives of each zone.

## Slide 7: Problem formulation
Flooded roads: disrupted
73 out of 138 edges are disrupted
Service roads

## Slide 8: Sets
I: Set of roads.
Dr Chen: What does a link represent? A route consisting of a set of roads connecting i and k?
If this is the case, then you are using a very cumbersome route-based formulation that unnecessarily complicates the problem.
Possible solutions: 1- Use of Paths or Routes: Instead of using individual links, define routes or shortest paths into critical facilities. Simplify the network representation by considering a subset of links that capture the critical paths or connections in the transportation network.
J: Set of access points or demand locations.
K: Set of critical infrastructure locations.
Z: Set of management zones.

## Slide 9: Parameters
Djk: Travel distance or time from access point j to critical infrastructure location k.
qj: Demand for access at point j to CF(can represent population).
fi: Repair or restoration cost for road i. (fi = Length (Road(i)) * unit cost)
Ek: Equity measure for infrastructure k.
Pz: Population or importance measure for zone z.
Ez: Desired equity level for zone z.
Bz: Budget or resource allocation for zone z.

## Slide 10: Decision Variables
Xijk: Binary decision variable indicating if access point j accesses critical infrastructure k through link i (1 if accessed).
yi: Binary decision variable indicating if road (link) i is repaired (1 if repaired, 0 otherwise).
Q: Dr Chen: What does a link represent? A route consisting of a set of roads connecting i and k?
If this is the case, then you are using a very cumbersome route-based formulation that unnecessarily complicates the problem.
Yes. 1- Use of Paths or Routes: Instead of using individual links, define routes or shortest paths from nodes into critical facilities. Simplify the network representation by considering a subset of links that capture the critical paths or connections in the transportation network. 2- Do some clustering work to make the problem decision variables based on zones instead of links (Roads). Based on 2022- An Equity-Based Optimization Model to Solve the Location Problem for Healthcare Centers …
From my perspective maybe we should calculate the length of the disrupted roads in each zone, or …

## Slide 11: One scenario to the question
Employing the use of paths or routes in an optimization framework involves defining and optimizing the restoration of specific paths or routes within the transportation network instead of individual links. This can significantly reduce the number of decision variables and simplify the modeling process.
1. Path or Route Definitions: Define paths or routes between demand nodes and critical facilities or other important points in transportation network. A path is a sequence of links that connects a node to a CF. Each path represents a potential route that can be restored.
2. Decision Variables: Introduce binary decision variables to represent whether a particular path or route is restored. Let P represent the set of paths. Define a binary decision variable for each path Rp for each path in P instead of link:
Rp= 1 if path p is restored, otherwise Rp = 0. Each Rp incorporates a set of link

## Slide 12: Objective Function 1 (Minimum cost)
Economic factors represent the budget and cost-related attributes incorporated in the planning such as direct or indirect costs.
Repair or Restoration Cost Component:
This component represents the cost associated with repairing or restoring link i in the zone z.
yiz is a binary decision variable (equal to 1 if link i is repaired, 0 otherwise) in zone z.
fiz is the repair or restoration cost for link i in zone z.
Q: Dr chen: what is this?
Link i belong to zone z

## Slide 13: Obj. 2 (Max traffic efficiency (Min travel time))
Travel time is the most frequently used metric to assess the quality of traffic service following disasters.
Repair or Restoration Cost Component:
Travel Cost Component:
This component represents the cost associated with traveling from access point j through road link i to critical infrastructure k.
xjik is a binary decision variable (equal to 1 if access point j accesses critical infrastructure k through link i, 0 otherwise).
djik is the travel time from access point j to healthcare k in road i.

## Slide 14: Obj. 2 (Max traffic efficiency (Min travel time))
l is the length of the road
There is a nonlinear relationship calculates the vehicle’s travel speed limit vd of road with different flood depths (Utkarsh 2022), and vf is the free flow speed.
The objective aims to minimize travel costs by optimizing access.
In summary, this objective function combines these components to find the optimal solution that minimizes repair costs, travel costs, and resource allocation costs.

## Slide 15: Obj. 2 (Max traffic efficiency (Min travel time))
Q: Again, is (i,j) a link or a route? This is not correct if you meant a route.
I meant a link (a road or street or …)
If we change our decision variables to route, then:

## Slide 16: One question
Is the following method logical if we consider nodes as decision variables?
Compute the shortest paths to the critical facilities for all demand nodes.
2. Calculate travel time, Roads ID, number of properties and households for each demand node, … for all demand zones
3. Calculate objective functions

## Slide 17: Cost Constraints: Resource Allocation
Ensure that resources are allocated within the available budget for each zone:
This constraint ensures that the total resources allocated for infrastructure restoration across all zones is higher than or equal to the total cost of restoration. A logical value can be assigned as the minimum amount of spendings, too.
In simpler terms, it enforces a resource allocation limit. The right-hand side of the inequality represents the total resources allocated to infrastructure restoration, considering factors associated with different zones. The left-hand side represents the total cost of restoration, considering the restoration cost for each infrastructure and whether it is restored (yi). The constraint ensures that you do not allocate more resources than what is needed to cover the restoration costs for all infrastructures.

## Slide 18: Cost Constraints: Resource Allocation
Q: Dr Chen: This does not make sense as you want to minimize it in objective 1.
It can. Actually, based on other objective functions like maximizing accessibility, the multi-objective model may choose to repair all roads or paths in non-dominated sorting solution. This constraint limits the feasible space to reasonable volume. However, if we do not have any value for the range of our monetary asset, we may relax this constraint and let the model choose even extreme solutions of choosing none of the paths (Min cost) or all of the paths (Max access).

## Slide 19: Access to infrastructures constraint
Q: Dr Chen: What does this mean?
This constraint is imposed to assure that at least a proportion of demand nodes population have access to critical infrastructures. Because non-dominated solutions of minimizing cost may lead to not selecting any road for repair (If we do not have any lower bound for cost constraint). However, this constraint can be replaced by lower limit of resource allocation constraint; Or, it can become another objective function.

## Slide 20: Equity-related Cost
Ei = Social Vulnerability Index
Q: The higher, the more vulnerable? Yes
“We adopt the social vulnerability index (SVI) created by the Centers for Disease Control and Prevention (CDC) in the study. The SVI considers four categories of community characteristics, including socioeconomic status, household composition disability, minority status language, and housing type transportation. The index is computed by synthesizing the aforementioned variables through the principal component analysis procedure (Cutter et al., Citation2012). The SVI is in the unit of census tract and can help us identify the communities that need support and attention before, during, and after a disaster (Flanagan et al., Citation2011). Because SVI is available at a census tract level, we use census tracts to approximate ‘community’ characteristics. We recognize that census tracts are an imperfect proxy for a community, as census tracts range in size from 1,200 to 8,000 people and may not follow jurisdictional or neighborhood boundaries.” + 4.1 section of (Utkarsh, 2022)

## Slide 21: Equity-related Cost
Equity Component:
This component represents the equity-related cost, which is incurred if road i is selected for retrofitting. The selected equity cost is higher for zones with less social vulnerability. Thus, the equity objective prefer to select roads for construction in more vulnerable areas.
Ei is an equity measure for Road i (e.g., SVI).
yi is a binary decision variable (equal to 1 if link i is repaired in time period t, 0 otherwise).

## Slide 22: Rawlsian maximin objective
The Rawlsian maximin principle, attributed to the political philosopher John Rawls, suggests maximizing the welfare or benefit of the least advantaged or most vulnerable group within a system. In the context of transportation network equity, it means prioritizing the improvement of links that serve critical facilities in a way that maximizes the minimum accessibility to these facilities.

## Slide 23: Rawlsian maximin objective
1- Calculate the proportion of population’s access to CF in the base case (before reconstruction) of each zone to the total population of the zone.
2- Select and prioritize the least advantaged zone as cz (Critical Zone)
3-

## Slide 24: Access to critical infrastructures
Access to infrastructures constraint can become a new objective function (soft constraint):
Accessibility Improvement Objective
Population Served: The number of people or entities served by the road to critical infrastructure can also be factored into the importance score. Infrastructures serving larger populations may receive a higher score.
Parameters:
xijk: Binary decision variable indicating if access point j accesses critical infrastructure k from road i (1 if accessed, 0 otherwise).
Popj: Number of populations in access point j.